x`	IMX6UL-Pheripheral Testing

USER LED GPIO
GPIO2_IO11:
root@RuggedBoard-iMx6:~# echo 43 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio43/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio43/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio43/value
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio43/value

GPIO2_IO12:
root@RuggedBoard-iMx6:~# echo 44 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio44/direction
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio40/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio44/value
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio44/value

GPIO2_IO13:
root@RuggedBoard-iMx6:~# echo 45 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio45/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio45/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio45/value
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio45/value

SWITCH:
root@RuggedBoard-iMx6:~# echo 40 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio40/direction
in
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio40/value
1
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio40/value
0

SD Card:
root@RuggedBoard-iMx6:~# [ 121.278632] mmc0: host does not support reading read-only switch, assuming write-enable
[ 121.294258] mmc0: new high speed SD card at address 0260
[ 121.313183] mmcblk0: mmc0:0260 1232 1.84 GiB
[ 121.339060] mmcblk0: p1 p2

root@RuggedBoard-iMx6:~# mount /dev/mmcblk0p1 /mnt/
[ 595.979213] FAT-fs (mmcblk0p1): Volume was not properly unmounted. Some data may be corrupt. Please run fsck.
root@RuggedBoard-iMx6:~# cd /mnt/
root@RuggedBoard-iMx6:/mnt# ls
backup

USB1:
root@RuggedBoard-iMx6:~# [ 185.424532] usb 1-1: new high-speed USB device number 2 using ci_hdrc
[ 185.629973] usb-storage 1-1:1.0: USB Mass Storage device detected
[ 185.655314] scsi host0: usb-storage 1-1:1.0
[ 186.727871] scsi 0:0:0:0: Direct-Access SanDisk Cruzer Blade 1.00 PQ: 0 ANSI: 6
[ 186.748728] sd 0:0:0:0: [sda] 61341696 512-byte logical blocks: (31.4 GB/29.3 GiB)
[ 186.774547] sd 0:0:0:0: [sda] Write Protect is off
[ 186.792551] sd 0:0:0:0: [sda] Write cache: disabled, read cache: enabled, doesn't support DPO or FUA
[ 186.837304] sda:
[ 186.846867] sd 0:0:0:0: [sda] Attached SCSI removable disk

root@RuggedBoard-iMx6:~# mount /dev/sda
sda sda1 sda2
root@RuggedBoard-iMx6:~# mount /dev/sda1 /mnt/
[ 458.814077] FAT-fs (sda1): Volume was not properly unmounted. Some data may be corrupt. Please run fsck.
root@RuggedBoard-iMx6:~#
root@RuggedBoard-iMx6:~# cd /mnt/
root@RuggedBoard-iMx6:/mnt# ls
upmexamples bckup

ETHERNET:
root@RuggedBoard-iMx6:~# [ 252.344439] fec 2188000.ethernet eth0: Link is Up - 100Mbps/Full - flow control rx/tx

root@RuggedBoard-iMx6:~# ifconfig eth0 192.168.1.12 up
root@RuggedBoard-iMx6~# ifconfig
eth0 Link encap:Ethernet HWaddr 50:2D:F4:10:82:69
        inet addr:192.168.1.12 Bcast:192.168.1.255 Mask:255.255.255.0
        inet6 addr: fe80::522d:f4ff:fe10:8269%lo/64 Scope:Link
        UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
        RX packets:63 errors:0 dropped:0 overruns:0 frame:0
        TX packets:48 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:4158 (4.0 KiB) TX bytes:7426 (7.2 KiB)

lo Link encap:Local Loopback
        inet addr:127.0.0.1 Mask:255.0.0.0
        inet6 addr: ::1%1/128 Scope:Host
        UP LOOPBACK RUNNING MTU:65536 Metric:1
        RX packets:6 errors:0 dropped:0 overruns:0 frame:0
        TX packets:6 errors:0 dropped:0 overruns:0 carrier:0
        collisions:0 txqueuelen:1000
        RX bytes:702 (702.0 B) TX bytes:702 (702.0 B)

root@RuggedBoard-iMx6:~# ping 192.168.1.12
PING 192.168.1.12 (192.168.1.12): 56 data bytes
64 bytes from 192.168.1.12: seq=0 ttl=64 time=0.759 ms
64 bytes from 192.168.1.12: seq=1 ttl=64 time=0.529 ms
64 bytes from 192.168.1.12: seq=2 ttl=64 time=0.530 ms
64 bytes from 192.168.1.12: seq=3 ttl=64 time=0.524 ms
64 bytes from 192.168.1.12: seq=4 ttl=64 time=0.530 ms
^C
--- 192.168.1.12 ping statistics ---
5 packets transmitted, 5 packets received, 0% packet loss
round-trip min/avg/max = 0.524/0.574/0.759 ms

RS-232
UART2_TX and UART2_RX:
root@RuggedBoard-iMx6:~# microcom -s 115200 /dev/ttymxc1
hiiiiiiiiiiiiiiii

UART2_CTS_B and UART2_RTS_B:
root@RuggedBoard-iMx6:~# microcom -s 115200 /dev/ttymxc0
hellooooooo

RS-485: (will work only board to board)
root@RuggedBoard-iMx6:~# microcom -s 115200 /dev/ttymxc5
haiiiiiiiiii

CAN:
root@RuggedBoard-iMx6:~# ip link set can0 down
root@RuggedBoard-iMx6:~# ip link set can0 type can bitrate 50000
root@RuggedBoard-iMx6:~# ip link set can0 up
root@RuggedBoard-iMx6:~# candump can0
  can0 123 [2] 12 67
^Croot@RuggedBoard-iMx6:~# cansend can0 123#1232

mPCIe Connector:

[ 7.582384] usb 2-1: new high-speed USB device number 2 using ci_hdrc
[ OK ] Found device /dev/ttymxc0.
[ 7.808849] usb 2-1: config 1 has an invalid interface number: 8 but max is 3
[ 7.816193] usb 2-1: config 1 has no interface number 1
[ 7.861806] qcserial 2-1:1.0: Qualcomm USB modem converter detected
[ 7.907296] usb 2-1: Qualcomm USB modem converter now attached to ttyUSB0
[ 7.948869] qcserial 2-1:1.2: Qualcomm USB modem converter detected
[ 7.987193] usb 2-1: Qualcomm USB modem converter now attached to ttyUSB1
[ 8.025386] qcserial 2-1:1.3: Qualcomm USB modem converter detected
[ 8.070908] usb 2-1: Qualcomm USB modem converter now attached to ttyUSB2
[ 8.120797] qmi_wwan 2-1:1.8: cdc-wdm0: USB WDM device
[ 8.166436] qmi_wwan 2-1:1.8 wwan0: register 'qmi_wwan' at usb-ci_hdrc.1-1, WWAN/QMI device, 2e:7c:9c:48:48:1b
[ OK ] Started udev Wait for Complete Device Initialization.

DIGITAL INPUT-
check if R63 resistor is mounted, and then connect 5pin connector to DigIN, connect a 5v or 12v adaptor to that connect vcc to vcc and ground to ground of 5pin connector.

Pin1-GPIO5-5:
root@RuggedBoard-iMx6:~# echo 133 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo in > /sys/class/gpio/gpio133/direction
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio133/value
echo in > /sys/class/gpio/gpio133/direction
1
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio133/value
0

Pin3-GPIO1-1:
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo in > /sys/class/gpio/gpio1/direction
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio1/value
1
root@RuggedBoard-iMx6:~# cat /sys/class/gpio/gpio1/value
0

DIGITAL OUTPUT-
Pin2-GPIO1_IO14:
root@RuggedBoard-iMx6:~# echo 14 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio14/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio14/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio14/value

Pin3-GPIO1_IO15:
root@RuggedBoard-iMx6:~# echo 15 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio15/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio15/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio15/value

Pin4-GPIO1_IO12:
root@RuggedBoard-iMx6:~# echo 12 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio12/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio12/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio12/value

Pin5-GPIO1_IO13:
root@RuggedBoard-iMx6:~# echo 13 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio13/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio13/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio13/value

RTC:
root@RuggedBoard-iMx6:~# date 013011542020.40
Thu Jan 30 11:54:40 UTC 2020
root@RuggedBoard-iMx6:~# hwclock -w -f /dev/rtc0
root@RuggedBoard-iMx6:~# hwclock -r -f /dev/rtc0
Thu Jan 30 11:55:00 2020 0.000000 seconds
root@RuggedBoard-iMx6:~# date
Thu Jan 30 11:55:04 UTC 2020

Mikro-BUS Connector-
Pin1-Analog Pin:
root@RuggedBoard-iMx6:~# cat /sys/bus/iio/devices/iio\:device0/in_voltage2_raw
4090

Pin 11 and Pin12:
root@RuggedBoard-iMx6:~# i2cdetect -y -r 0
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- UU -- -- -- -- -- -- -- 5a -- -- -- -- --
60: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
70: -- -- -- -- -- -- -- --
root@RuggedBoard-iMx6~# i2cdetect -y -r 0
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- 18 -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- UU -- -- -- -- -- -- -- 5a -- -- -- -- --
60: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
70: -- -- -- -- -- -- 76 --

Expansion Header-
Pin5:
root@RuggedBoard-iMx6:~# echo 13 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio13/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio13/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio13/value

Pin7:
root@RuggedBoard-iMx6:~# echo 12 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio12/direction
root@pRuggedBoard-iMx6~# echo 1 > /sys/class/gpio/gpio12/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio12/value

Pin9:
root@RuggedBoard-iMx6:~# echo 15 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio15/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio15/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio15/value

Pin11:
root@RuggedBoard-iMx6:~# echo 14 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio14/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio14/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio14/value

Pin14-SPI2_MISO and PIN16-SPI2_MOSI:
root@RuggedBoard-iMx6:~# ./spidev_test -D /dev/spidev1.0
spi mode: 0
bits per word: 8
max speed: 500000 Hz (500 KHz)

FF FF FF FF FF FF
40 00 00 00 00 95
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
DE AD BE EF BA AD
F0 0D
root@RuggedBoard-iMx6:~# ./spidev_test -D /dev/spidev1.0
spi mode: 0
bits per word: 8
max speed: 500000 Hz (500 KHz)

FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF

Pin20-PWM:
root@RuggedBoard-iMx6:~# cat /sys/class/pwm/pwmchip0/npwm
1
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/pwm/pwmchip0/export
root@RuggedBoard-iMx6:~# cat /sys/class/pwm/pwmchip0/pwm0/polarity
normal
root@RuggedBoard-iMx6:~# echo 5000 > /sys/class/pwm/pwmchip0/pwm0/period
root@RuggedBoard-iMx6:~# echo 4000 > /sys/class/pwm/pwmchip0/pwm0/duty_cycle
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/pwm/pwmchip0/pwm0/enable
root@RuggedBoard-iMx6:~# cat /sys/kernel/debug/pwm
platform/2088000.pwm, 1 PWM device
 pwm-0 (sysfs ): requested enabled period: 5000 ns duty: 4000 ns polarity: normal
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/pwm/pwmchip0/pwm0/enable

Pin23 and Pin25-Uart3:
root@RuggedBoard-iMx6:~# microcom -s 115200 /dev/ttymxc2
Helloooooooooooo

Pin24-SPI1_MISO and PIN26-SPI1_MOSI:
root@RuggedBoard-iMx6:~# ./spidev_test -D /dev/spidev0.0
spi mode: 0
bits per word: 8
max speed: 500000 Hz (500 KHz)

FF FF FF FF FF FF
40 00 00 00 00 95
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
DE AD BE EF BA AD
F0 0D
root@RuggedBoard-iMx6:~# ./spidev_test -D /dev/spidev0.0
spi mode: 0
bits per word: 8
max speed: 500000 Hz (500 KHz)

FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF FF FF FF FF
FF FF

Pin28-I2C1_SCL and Pin30-I2C1_SDA:
root@RuggedBoard-iMx6:~# i2cdetect -y -r 0
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- UU -- -- -- -- -- -- -- 5a -- -- -- -- --
60: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
70: -- -- -- -- -- -- -- --
root@RuggedBoard-iMx6:~# i2cdetect -y -r 0
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- 18 -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- UU -- -- -- -- -- -- -- 5a -- -- -- -- --
60: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
70: -- -- -- -- -- -- 76 --

Pin29:
root@RuggedBoard-iMx6:~# echo 46 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio46/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio46/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio46/value

Pin31:
root@RuggedBoard-iMx6:~# echo 11 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio11/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio11/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio11/value

Pin32-I2C2_SCL and Pin34-I2C2_SDA:
root@RuggedBoard-iMx6:~# i2cdetect -y -r 1
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
60: -- -- -- -- -- -- -- -- UU -- -- -- -- -- -- --
70: -- -- -- -- -- -- -- --

root@RuggedBoard-iMx6:~# i2cdetect -y -r 1
     0 1 2 3 4 5 6 7 8 9 a b c d e f
00: -- -- -- -- -- -- -- -- -- -- -- -- --
10: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
20: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
30: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
40: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
50: -- -- -- -- -- -- -- -- -- -- -- -- -- -- -- --
60: -- -- -- -- -- -- -- -- UU -- -- -- -- -- -- --
70: -- -- -- -- -- -- 76 --

Pin35:
root@RuggedBoard-iMx6:~# echo 10 > /sys/class/gpio/export
root@RuggedBoard-iMx6:~# echo out > /sys/class/gpio/gpio10/direction
root@RuggedBoard-iMx6:~# echo 1 > /sys/class/gpio/gpio10/value
root@RuggedBoard-iMx6:~# echo 0 > /sys/class/gpio/gpio10/value